## Slide 1: REDD FHMM Exploration
CMSC 123

## Slide 2: Description of FHMM Application from REDD Paper
In the FHMM, each of the n devices (or circuits) in the home is described via a Hidden Markov Model (HMM). Each device has a discrete hidden state, denoted x(i) t ∈ {1,...,Ni} for the state at time t for device i, which corresponds roughly to the internal state of the device (“oﬀ”, or in one of several possible “on” states). At each time t, given the internal state, the ith device emits a Gaussian- distributed power, denoted y(i) t , with state-speciﬁc mean and variance parameters. However, we only observe the sum of all the power outputs at each time, ¯ yt = Pn i=1 y(i) t . The disaggregation task can then be framed as an inference problem: given an observed sequence of aggregate energy ¯ y1,..., ¯ yT , we aim to compute the posterior probability of the individual device consumptions y(i) t , i = 1,...,n, t = 1,...,T. A graphical model depicting representing this FHMM is shown in Figure 7.

## Slide 3: FHMM Description: Joan’s Version
For each device in a house i , we can describe its state x at time t using x(i) t ∈ {1,...,Ni} , where x is off, or one of the states of “on”.
At each time t, the ith device will be using power y(i)t.
We can only observe the sum of power being used for all devices at time t, or Yt = sum(y(i)t).
So the problem is: given a series of aggregated outputs Yt from time t =1 to time t =T, can we compute the probability of y(i)t for each device i at time t ∈ {1,...,T}?

## Slide 4: REDD FHMM Method
To build the model from data we use the individual appliance energy sequences, as collected by the individual device monitors, and train HMMs using the standard Baum-Welch (EM) algorithm (thus, the algorithm we are describing falls under the“supervised”designation of Section 2). Exact posterior inference in the FHMM model is not tractable (we use 4 states per device, and typically around 20 devices per home for a total of 420 ≈ 1 × 1012 diﬀerent combinations of hidden states), so we use a blocked Gibbs sampling scheme: we ﬁx the hidden states of all but one of the chains, resulting in a Gaussian posterior over the emissions over the remaining chain; at this point, we can eﬃciently sample over hidden states for the held-out chain, and repeat the process until the distribution over all hidden states mixes. (We also anneal the sampling procedure by artiﬁcially inﬂating the variance of the observed aggregate outputs during the early iterations of Gibbs sampling.)

## Slide 5: FHMM Method: Joan’s Version
To train their model, they used the available information: y(i)t from their devices, which is what we have in the dataset.
The model was trained with the standard Baum-Welch (EM) algorithm (???).
Since they have a lot of data, they had to use a “Gibbs blocking sample”:
  Fix the hidden states of all but one of the chains(?)
  Sample(?) over hidden states for the held-out chain
  Repeat the process until the distribution over all hidden states mixes (?).

## Slide 6: Baum Welch Algorithm
http://ocw.mit.edu/courses/aeronautics-and-astronautics/16-410-principles-of-autonomy-and-decision-making-fall-2010/lecture-notes/MIT16_410F10_lec21.pdf
It seems like it’s basically a way to take an HMM model, defined lambda = (T, M, pi) to construct a new and better HMM model, using a series of matrix transformations on T, and M.

## Slide 7: More on the HMM
Haha who wants to read this paper (though they do have pseudo code): http://www.cs.sjsu.edu/faculty/stamp/RUA/HMM.pdf

## Slide 8: REDD Evaluating FHMM Results
To evaluate the method, we used 2 weeks of data from 5 of the houses in REDD; since the plug-level monitors had not yet collected suﬃcient data at the time of writing, we use the whole-home and circuit level data. A description of the devices in each of these homes is given in Table 1. In the presented experiments we sub-sampled the data to 10 second intervals using a median ﬁlter. To evaluate the performance of the method, we used the“total energy correctly assigned” metric described in Section 2, deﬁned formally as
Acc = 1 −
PT t=1 Pn i=1 y(i) t − y(i) t 2PT t=1 ¯ yt
where ˆ y(i) t denotes the algorithm’s prediction for the ith de- vice at the tth time step, and where the 2 factor in the denominator comes from the that that the absolute value will “double count” errors, since Pn i=1 y(i) t = Pn i=1 ˆ y(i) t .

## Slide 9: Evaluating FHMM Results: Joan’s Version
To see how accurate their model was, they tested their results against a subsample of their data (pulled using a “median filter”, 10 sec. intervals)
Their metric is “total energy correctly assigned”(Acc); see report for formula. It’s 1 – the sum of the difference of predicted y and actual y for all devices at all times, divided by 2*the sum of the total power Y at each time t. Basically an average percent error.

## Slide 10: REDD Paper: Testing Procedures
Table 2 shows the disaggregation performance of the FHMM model on the ﬁve houses we consider. We focus on two test- ing procedures: in the ﬁrst case we build HMM models from devices in a given house, and then attempt to disaggregate energy in that house; in the second case, we train on four of the houses and test on the remaining held-out house. This procedure is analogous to “training” versus “testing” error, and we label the results accordingly in Table 2. For com- parison we also show the performance of a simple mean pre- diction algorithm, which estimates the total percentage that each device type consumes and predicts that the total energy breaks down according to this percentage at all times.

## Slide 11: Testing Procedures: Joan’s Version
First procedure: Only used data from one house, built models for that one house
Second procedure: Trained on data from 4 houses, then tested on 5th house.
Question: Which procedure should we use?